## Slide 1
ChillStream
Phase-Change Thermal Battery Water Dispenser
Cold water for the 50th person in line — not just the first.
Executive Overview • Product Investment Proposal • 2026

## Slide 2
The Problem
Water coolers fail at the moment of peak demand
School lunch bell rings — 60 students, 5 minutes
Office break time — 30 people cluster at the cooler
Traditional cooler: 2-5L of pre-chilled water
After 10-15 pours, reservoir is depleted
Incoming mains water at 25°C mixes with remaining cold
Recovery time: 20-40 minutes
The first users get cold water.
Everyone else gets lukewarm.
20-40 min
Recovery time after peak demand depletes the reservoir
85%+
Of pours during rush hour served above target temperature
$0
Revenue from solving this — no product addresses peak demand in countertop form factor

## Slide 3
The Solution: Phase-Change Thermal Battery
Store
IDLE TIME
Compressor freezes PCM coating on submerged HX plates to -5°C. Cold energy stored as latent heat. No water movement needed.
Deliver
PEAK DEMAND
User opens tap. Mains pressure pushes water through PCM-coated plates. Water chills from 25°C to 4°C on contact. No pump.
Recover
BETWEEN RUSHES
Compressor recharges the PCM. 33 min for full 5L recharge. Partial recharge much faster. 50-min school period = full reset.
Latent heat stores 5-10x more energy per kg than sensible heat — enabling countertop form factor with 50-pour capacity.

## Slide 4
Product Architecture
1
Insulated Tank
Simple SS vessel Holds water at rest Open top, sealed by cover Serviceable — lift cover to clean
No pressure rating needed No embedded channels Food-grade stainless steel
2
Submerged Plate HX
Brazed SS plates with PCM coating (-5 to -10°C) Refrigerant channels freeze PCM Water channels chill on pour
Standard component (Kaori, SWEP) Scales by plate count: 4 plates = 5L | 8 plates = 10L
3
Cover / Manifold
Routes all fluid connections: • Mains water in (top) • Chilled water out (to tap) • Refrigerant lines (to HX)
Only complex manufactured part Lifts off for full tank access Injection-molded + brazed fittings
Key design principle:
Water moves only when the tap is open (mains pressure driven). No circulation pump. The cover is the single point of service — lift it off, and the tank is accessible for cleaning. The HX comes out with the cover.

## Slide 5
Inside ChillStream
Annotated cross-section — all major subsystems visible. Section references map to the system description document.

## Slide 6
Fleet-First IoT Platform
Fleet Dashboard
Real-time monitoring
Temperatures, capacity %, compressor state across all units
Usage analytics
Pours/day, peak times, demand vs. capacity — sizing recommendations
Predictive maintenance
Compressor anomaly detection, condenser fouling alerts
Filter management
Fleet-wide filter life tracking, replacement scheduling
OTA firmware updates
Staged rollout, automatic rollback, zero downtime
Remote commands
Reboot, config push, maintenance mode, diagnostics
On-Unit Display
• Cold capacity gauge (% remaining)
• Live output temperature during pour
• Filter life indicator
• Recharge ETA when capacity is low
• PIN-protected operator settings
Connectivity
• WiFi (ESP32-S3, built-in — $0 extra HW)
• MQTT telemetry + HTTPS for OTA/config
• TLS 1.3, X.509 device certificates
• Works fully offline — buffers 7 days locally
• AP mode captive portal for setup

## Slide 7
Market Opportunity
Schools (K-12)
130,000+ in the US alone
Peak demand at every bell — the hardest use case. Budget-sensitive. Fleet purchases by district.
$800-1,100
per unit
Offices
~1M commercial offices in US
Steady use with lunch/break clusters. Facility managers want zero-maintenance.
$600-900
per unit
Healthcare / Clinics
~230,000 medical offices
Waiting rooms, staff areas. Hygiene and compliance matter.
$800-1,100
per unit
Hospitality
Hotels, coworking, airports
High-visibility locations. Premium positioning possible.
$900-1,200
per unit
Entry point: Schools (hardest use case = best proof point) and offices (highest volume).

## Slide 8
Unit Economics
5L MODEL — BOM BREAKDOWN
Cold assembly (tank + HX + cover + PCM)
$75
30%
Refrigeration system
$50
20%
Hot water system
$25
10%
Water path (valves, flow sensor, filter housing)
$20
8%
Electronics (ESP32, PCB, sensors, relays, PSU)
$25
10%
Display + UI
$15
6%
Enclosure + packaging + misc
$43
17%
Materials subtotal
$253
Assembly + test + brazing + scrap (5%)
$133
TOTAL COGS — 5L UNIT
$386
5L Model
$749
COGS: $386
Gross margin: 48%
Offices, small clinics
10L Model
$999
COGS: $442
Gross margin: 56%
Schools, large offices
Filter Cartridge
$20
COGS: $6 | Margin: 70%
2-3 replacements/year per unit
NFC tag for auto lifecycle tracking
Proprietary twist-lock (recurring revenue)

## Slide 9
Recurring Revenue Model
Two recurring streams per unit:
Filter cartridges
$20/cartridge × 2-3/year = $40-60/unit/year
70% gross margin. Proprietary twist-lock with NFC.
Cloud SaaS (optional)
$10/month/unit = $120/unit/year
85% gross margin. Fleet dashboard, analytics, OTA.
Combined: $160-180/unit/year
ANNUAL RECURRING AT FLEET SCALE
10 units
$1,600-1,800
Single site (small office building)
50 units
$8,000-9,000
School district or multi-floor office
100 units
$16,000-18,000
Regional facility operator
500 units
$80,000-90,000
National FM company
1,000 units
$160,000-180,000
Enterprise account
Hardware is the door opener. Recurring revenue is the business model.
At 1,000 deployed units, annual recurring exceeds initial hardware revenue within 12-18 months of fleet buildout.

## Slide 10
Why ChillStream Wins
Physics advantage
Latent heat stores 5-10x more energy than sensible heat per kg. A 3 kg PCM mass replaces a 15-20L cold water tank. This is why we fit in a countertop form factor.
No moving parts in the water path
No pump, no circulator. Water moves on mains pressure only. Fewer failure modes. Lower cost. Silent during dispense.
Standard components, novel assembly
The plate HX is off-the-shelf (Kaori, SWEP). The compressor is catalog (Secop, Embraco). The tank is a simple vessel. The innovation is in the assembly and the PCM coating — not in reinventing the parts.
Fleet-first IoT from day one
Built for operators managing 10-1,000 units. Not a consumer gadget with an app bolted on. Predictive maintenance, sizing recommendations, OTA updates, compliance reporting.
Recurring revenue built into the product
Proprietary filter with NFC lifecycle tracking. Cloud SaaS for fleet management. Combined: $160-180/unit/year at 70-85% margin.

## Slide 11
Roadmap & Key Risks
18-MONTH DEVELOPMENT ROADMAP
M1-M3
PCM + HX prototype
Material selection, thermal simulation, bench prototype of submerged plate HX
M4-M6
Full functional prototype
Complete unit: cold + hot + electronics + display + WiFi
M7-M9
EVT
Engineering validation. Performance testing. Begin certification.
M10-M12
DVT
Design validation. Reliability testing. 10,000-cycle PCM test.
M13-M14
Pilot fleet
5-10 units deployed in real schools and offices. Field data.
M15-M18
PVT → Production
Manufacturing validation. Certification complete. Ship.
TOP RISKS & MITIGATIONS
PCM encapsulation durability
Can coated plates survive 10,000+ freeze-thaw cycles? → Material science partnership + accelerated life test by M3
HX thermal performance
Can 4 plates achieve 25°C→4°C at 1 L/min? → Thermal simulation + bench prototype by M3
Cover manifold complexity
Single part routes water + refrigerant + sensors. → Industrial design + mechanical prototype by M4
Mineral fouling
HX plates always submerged in water. → Upstream filter + descaling protocol + accelerated fouling test

## Slide 12
The Ask
Phase 1: Prove the Physics
M1-M6
$250K
PCM material selection and encapsulation testing
Submerged plate HX thermal prototype
Cover manifold mechanical prototype
Full functional prototype (1 unit)
Thermal performance validation
Phase 2: Validate the Product
M7-M14
$400K
EVT + DVT (10-20 units)
Certification (UL, NSF, FCC/CE)
IoT platform development (dashboard, OTA)
Pilot fleet: 5-10 units in real deployments
Field data collection and iteration
Phase 3: Scale to Market
M15-M18+
$350K
PVT and production tooling
Manufacturing line setup
First 500-unit production run
Sales team and channel partnerships
Launch marketing
Total investment to production:
$1M over 18 months